# A 70 HINGED PVC system

Supply and fitting of 16 mm groove windows/doors comprising of PVC profiles that, according to its design and dimensions, ensures the system’s resistance and the ability to keep its shape.

It has a frame depth of 70 mm and 70/80 mm in the sash with 5 internal chambers both in sash as in frame.

Categories achieved at test bed*:

Air permeability according to UNE-EN 12207:2000 norm	 	Class  4

Water tightness according to UNE-EN 12208:2000 norm                Class  E1800

Wind resistance according to UNE-EN 12210:2000 norm                Class  C5

* Test reference on a double sash window measuring 1.30 x 1.30 mts

Surface finish:

Surface of (colour …………, imitation timber ……….) achieved by way of a lamination on the base profile with a high resistance solar radiation thermo welded film that has been tested on an accelerated ageing test bed.